## Slide 1: Introduction to Diode and Diode Logic Gates
Course No: CSE 251
Course Title: Electronic Devices and Circuits
Lecture 7
Course instructor:
Aroni Ghosh (ARG)
Lecturer, CSE, Brac University

## Slide 2: Introduction to Diode
A two terminal Non-linear device. The two terminals are: Anode (+) and Cathode(-)
The voltage difference between the terminals is expressed as, Vd= Vanode –Vcathode
The working principle of a diode can be expressed with an “Electronic Valve”. It only allows the current to flow in one direction (From Anode to Cathode). This means the diode is “ON”/ in Forward Bias only when Vd is positive (Vanode > Vcathode). This property makes it suitable as a “Rectifier”
https://www.geeksforgeeks.org/diode/

## Slide 3: Ideal diode model and IV characteristics
In the Ideal diode model, the following conditions are assumed:
i. Vanode>Vcathode:
-The Diode will be ON - It will act as a “Short circuit”
ii. Vanode<Vcathode:
-The Diode will be OFF
- It will act as a “Open circuit”
Open circuit I-V: x axis
Short Circuit I-V: y axis

## Slide 4: Real Diode I-V
In the Real diode model, the following conditions are assumed:
i. Vd>Vthreshold:
-The Diode will be ON
- It will act as a “Constant Voltage Source”
ii. Vd< Vthreshold:
-The Diode will be OFF
- It will act as a “Open circuit”
Open circuit I-V: x axis
Constant Voltage Source I-V: parallel to y axis

## Slide 5: p-n junction Diode
P-type semiconductor: When an intrinsic or pure semiconductor material (Like, Silicon (Si) and Germanium (Ge)) doped with acceptor impurities atom (Trivalent atoms, like Boron (B), Gallium (G), Aluminium(Al))
N-type semiconductor: When pure semiconductor doped with donor impurities (Pentavalent atoms, like Phosphorus (P), Arsenic (As), Antimony (Sb))

## Slide 6: p, n type semiconductor
p- type
n- type
https://toshiba.semicon-storage.com/ap-en/semiconductor/knowledge/e-learning/discrete/chap1/chap1-4.html

## Slide 7: p-n junction
Threshold voltage- for silicon about 0.7V
- for germanium about 0.3V.
https://byjus.com/physics/p-n-junction/

## Slide 8: Shockley Diode Equation
Where IS is reverse saturation current
Where VT is Thermal Voltage

## Slide 9: Example Problems (Ideal Diode)
Example 1:
Vanode= 5V
Diode is on replace with short circuit (Ideal Diode Model)
Vo= V= 5V
I= Vo/R= 5V/2.5k= 2 mA

## Slide 10: Example Problems (Ideal Diode)
Example 2:
Vcathode= 5V
Diode is off replace with open circuit (Ideal Diode Model)
As the circuit is open, I= 0 mA
Vo= 0V

## Slide 11: Example Problems (Ideal Diode)
Example 3:
Vcathode= -5V
Diode is on replace with short circuit (Ideal Diode Model)
Vo= -5V
I= Vo/R= -5V/5k= -1 mA

## Slide 12: Logical Operations with Diode (OR)
Logic Truth Table
Voltage Truth Table
Low/False High/True
Logic Levels: 0 1
Corresponding voltage levels: 0V 5V

## Slide 13: Logical Operations with Diode (OR)
Case 1: VA= 0V, VB= 0V
Both D1 and D2 are off as Vanode<Vcathode
Replace D1 and D2 with open circuits.
So, VC= 0V
D1
D2
R is a Pull Down Resistor which pulls down the voltage of VC from floating condition to 0V.

## Slide 14: Logical Operations with Diode (OR)
Case 2: VA= 0V, VB= 5V
D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit.
So, VC= VB= 5V
Case 3: VA= 5V, VB= 0V
D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit.
So, VC= VA= 5V
Case 1: VA= 5V, VB= 5V
Both D1 and D2 are on
Replace D1 and D2 with short circuits.
So, VC= VA= VB= 5V

## Slide 15: Logical Operations with Diode (AND)
Logic Truth Table
Voltage Truth Table

## Slide 16: Logical Operations with Diode (AND)
Case 1: VA= 0V, VB= 0V
Both D1 and D2 are on as Vanode>Vcathode
Replace D1 and D2 with short circuits.
So, , VC= VA= VB= 0V
D1
D2
R is a Pull Up Resistor which pulls up the voltage of VC from floating condition to 5V.

## Slide 17: Logical Operations with Diode (AND)
Case 2: VA= 0V, VB= 5V
D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit.
So, VC= VA= 0V
Case 3: VA= 5V, VB= 0V
D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit.
So, VC= VB= 0V
Case 1: VA= 5V, VB= 5V
Both D1 and D2 are off
Replace D1 and D2 with open circuits.
So, VC= 5V

## Slide 18: Effect of input Voltage Variation in Logic Gates (OR)
D1
D2
Case 1: Assuming both D1 and D2 are on
Replace D1 and D2 with short circuits.
So, VC is short with both VA and VB
Can VC be 4V and 5V at the same time???
So this assumption is wrong!
If VA= 4V and VB= 5V, what is the value of output VC?

## Slide 19: Effect of input Voltage Variation in Logic Gates (OR)
Case 2: Assuming both D1 and D2 are off
Replace D1 and D2 with open circuits. So, VC= 0V
But now Vanode(4V for D1, 5V for D2)>Vcathode(0V) for both diode
So this assumption is also wrong!
Case 3: Assuming D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit. So, VC= VA= 4V
But now for D2, Vanode(5V)>Vcathode(4V). So, D1 should have been ON!
So this assumption is also wrong!
Case 4: Assuming D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit. So, VC= VB= 5V
Now for D1, Vanode(4V)<Vcathode(5V). So, D1 should be OFF!
So this assumption is correct!

## Slide 20: Effect of input Voltage Variation in Logic Gates (OR)
Example 4: Find the value of Vo
D1 and D2 are OFF  Open Circuit
Only D3 is ON  Short Circuit
Vo= 4.5V
Current, I= 4.5V/2k= 2.25 mA

## Slide 21: Effect of input Voltage Variation in Logic Gates (AND)
Case 1: Assuming both D1 and D2 are on
Replace D1 and D2 with short circuits.
So, VC is short with both VA and VB
Can VC be 1V and 2V at the same time???
So this assumption is wrong!
If VA= 1V and VB= 2V, what is the value of output VC?

## Slide 22: Effect of input Voltage Variation in Logic Gates (AND)
Case 2: Assuming both D1 and D2 are off
Replace D1 and D2 with open circuits. So, VC= 5V
But now Vanode(5V)>Vcathode(1V for D1 & 2V for D2) for both diode
So this assumption is also wrong!
Case 4: Assuming D1 is on and D2 is off
Replace D1 with short circuit and D2 with open circuit. So, VC= VA= 1V
Now for D2, Vanode(1V)<Vcathode(2V). So, D2 should be OFF!
So this assumption is correct!
Case 3: Assuming D1 is off and D2 is on
Replace D1 with open circuit and D2 with short circuit. So, VC= VB= 2V
But now for D1, Vanode(2V)>Vcathode(1V). So, D1 should have been ON!
So this assumption is also wrong!

## Slide 23: Effect of input Voltage Variation in Logic Gates (AND)
Example 5: Find the value of Vo
D1 and D2 are OFF  Open Circuit
Only D3 is ON  Short Circuit
Vo= -5V
= 5 mA

## Slide 24: Thank You